## Slide 1
(A) Uncertain SS316
material-property inputs
8 parameters with
Gaussian priors (10% CoV)
Elasticity
E_slope
E_intercept
ν
Thermal expansion
α_base
α_slope
Thermal transport
T_ref^SS316
k_ref^SS316
α_SS316
All parameters are treated as
probabilistic priors, not constants.
(B) Coupled high-fidelity simulation
OpenMC neutronics + FEniCS
thermo-mechanics
Uncoupled pass
Coupled steady response
OpenMC
(neutronics)
FEniCS
(thermo-mechanics)
Temperature
Preliminary stress
OpenMC
(updated power)
FEniCS
(thermo-mechanics)
Temperature
von Mises stress
Geometry / deformation update
Training dataset:
3,341 filtered HF samples
3,418 generated before filtering
Train: 2,339
Validation: 501
Test: 501
(C) Bayesian neural surrogate
Unified posterior predictive layer
Physics-regularized Bayesian
neural network
...
...
8 inputs
254
254
15 scalar outputs
Posterior predictive distribution
p(y | x, D)
Output space
Predictive mean
90% predictive interval
Trained once; used without modification
for all downstream analyses.
(D) Downstream analyses
three coherent applications
1
Forward uncertainty propagation
Monte Carlo propagation through
posterior predictive samples
Uncertain
inputs
Output distribution
(uncertainty quantified)
2
Variance-based sensitivity attribution
Sobol S1 and ST indices
Sobol index
Input parameters
S1 (first-order)
ST (total-order)
3
Observation-conditioned
posterior calibration
MCMC parameter updating
using HF observations
Prior
Posterior
Primary role of the surrogate: a unified posterior predictive layer enabling forward uncertainty propagation, variance-based attribution, and observation-conditioned posterior updating.